## Slide 1
HEALTH +
IoT Enabled Ubiquitous Healthcare Data Acquisition and Monitoring System
By
Shubham Sanjay Sonawane
Guided By
Prof. Vidhaydhar J Aski
(Manipal University, Jaipur)

## Slide 2: Problem Statement
“Health monitoring, heart monitoring, rehabilitation, and assisted living for the elderly and medically challenged people on domestic basis.”

## Slide 3: Proposed System
Various body sensors are connected to a microcontroller to track the status
Private Wi-Fi connection is used in order to transmit collected data and receive user requests.
This data is then shared with doctors through a web application.
Doctor can analyze the condition of the patient and provide further details online.
Patient or doctor can communicate with each other and view the past data any time they want.

## Slide 4: Requirements
Hardware
Software
Arduino Uno
NodeMCU
Temp Sensor
Pulse Rate Sensor
ECG Module
OLED Display
Jumper Wires
Breadboard
Arduino IDE
Embedded C
Node.js
HTML, CSS and JavaScript
Python
MongoDB
Heroku
Git

## Slide 5: Hardware Model
Sensors
DS18B20 - Digital temperature sensor.
High accuracy digital temperature sensor ideal for Body Temperature Measurement.
SEN-11574 Pulse rate sensor.
Popular infrared pulse rate sensor with analog output.
AD8232 ECG Module
AD8232 is low power 3.3 v device with inbuilt noise cancelation unit.
Microcontrollers
Arduino Uno
For sensor management
Node MCU
Inbuilt ESP8366 for Network Management.

## Slide 6: System Architecture

## Slide 7: Circuit Diagram

## Slide 8
Start
Initialize Pin 8 to DS18B20
Initialize Pin 9,10 to AD8232 A,B
Initialize and A1 to AD8232 analog
Read Incoming Serial Data
If Serial Read Requested
Temp
Pulse
ECG
X1
DS18B2 Temp Sensor function
SEN-11574 Pulse Sensor
function
ECG Sensor function
X1 Sensor function
Delay 500 ms
Arduino Uno Flow Chart
Write Outgoing Serial Data

## Slide 9
Start
Initialize Wi-Fi Client Object
Initialize Wi-Fi Server Object
Initialize and Wi-Fi name and password
User HTTP Request Available
Delay 1000 ms
(wait for serial)
If Serial Incoming Available
Print data on Display and Send HTTP request with data to cloud server.
Delay 500 ms
End
Write Sensor Request on Outgoing Serial
NodeMCU Flow Chart
Wait for Request

## Slide 10
Result And Observation Of Temperature Sensor
Chart: 
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40
Internal Temp | 87.44 | 88.7 | 89.24 | 90.68 | 93.02 | 93.38 | 93.02 | 93.02
Time (Sec)
Temperature
(°F)

## Slide 11
Approach And Observation Of Pulse Rate Sensor
T1
T2
ΔT
550
Analog Input
Time
Threshold
ΔT = T1 – T2
F = 1 / ΔT Beats/sec
= 1 / ΔT * 60 BPM
Where,
T1 = Time of first beat
T2 = Time of Second beat
ΔT = Time Difference
F = Pulse Frequency

## Slide 12
Electrodes Near Heart
Electrodes Away Heart
ECG Result And Observation

## Slide 13: ECG Processing

## Slide 14: Software
The software consist of web application and android application located on cloud.
We are done with the development of user interface of the website using basic web technology (HTML, JavaScript, CSS).
The middleware of the website will be developed using Node.js.
Technologies like Ajax and Web Sockets are to be used for real time update.
The Database will be developed in a document based databases like Mongo DB or Kairos DB.
This type of databases are highly compatible with JavaScript based technologies like Node.js. They allow us fetch data using query less techniques like Rest API.

## Slide 15: Database
Users Collection
"User”: {
"User ID”: INT,
"Name”: STR,
"Email”: STR,
"DOB”:STR,
"Password”: STR,
"Phone”: INT,
"Chronic-Diseases”: STR,
"Blood-Group”: STR,
"Weight”: INT,
"Height”: INT,
"Description”: INT,
"My-Doctor”: Doctor
}
Doctors Collection
"Doctor" {
"Doctor ID”: INT,
"Name”: STR,
"Hospital”: STR,
"Phone”: INT,
"Email”: STR,
"Password”: STR,
"Qualification”: STR,
"Specialization”: STR,
"Patients”: Array<User>
}
Health Parameter Collections
"Temperature" {
"User ID”: INT,
"Time-Stamp”: INT,
"Data”: INT
}
“Pulse-Rate" {
"User ID”: INT,
"Time-Stamp”: INT,
"Data”: INT
}
"ECG" {
"User ID”: INT
"Time-Stamp”: INT,
"Data"
}

## Slide 16: Data Flow

## Slide 17: Web Application Screens
Login Page
Home Page
Doctors
Doctor’s Profile
Patient Profile
Temperature Page
Pulse rate Page
ECG Diagnosis

## Slide 31: Live Web-App Link
https://health-plus-web.herokuapp.com
Publication
https://link.springer.com/chapter/10.1007/978-981-13-1280-9_1

## Slide 32
Code Base

## Slide 33: Conclusion And Future Work
More sensors like body composition sensors, blood pressure, insulin and sugar monitor, RBC, WBC and platelet monitors can be added to the system
The system can be made compatible with popular home Automation AI like Google Home’s Google Assistant and Amazon Echo’s Alexa to provide more immersive experience.
System can be integrated with a wearable devices to ease the task.

## Slide 34: Thank You